DRYING KINETICS, MATHEMATICAL MODELING AND VOLUMETRIC SHRINKAGE OF SUNFLOWER SEEDS (HELIANTHUS ANNUUS L.)

Paulo Carteri Coradi*, Jean Carlos Helmich, Carlos Henrique Portela Fernandes2, Clayton Cerqueira Peralta2

ABSTRACT: Given the prominence of sunflower on the national scene and the importance of the drying step for post-harvest, this study aimed to evaluate the drying kinetics of sunflower seeds in an oven with forced convection and forced air for different temperatures, mathematically describe and determine the effects of drying on shrinkage of seeds. The experimental design was completely randomized, factorial (4x3), four drying air temperatures (45, 55, 65 and 75 °C) and three replications. Drying was carried out until the water content of the seeds comes into equilibrium moisture. The temperature and air flow were monitored with the aid of a psychrometer, and a hot wire anemometer, respectively. It has been found, the results obtained that the drying time was significantly (P<0.05) reduced with increasing temperature of the drying air. The model of Wang and Sing was that better adjusted to experimental drying data. Effective diffusivity of sunflower seed ranged from 2.83 to 2.93x10-6 m2 s-1, while the isosteric heat of adsorption was 3,725.176 to 3,773.082 kJ kg-1. Reducing the water content influenced the shrinkage of sunflower seeds, with emphasis on temperatures above 55 °C. The model Correa et al. was that better adjusted to experimental data of volumetric shrinkage of sunflower seeds.

KEYWORDS: dryer, optimization, post-harvest.

CINÉTICA DE SECAGEM, MODELAGEM MATEMÁTICA E CONTRAÇÃO VOLUMÉTRICA DE SEMENTES DE GIRASSOL (HELIANTHUS ANNUUS L.)

RESUMO: Diante do destaque da cultura do girassol no cenário nacional e da importância da etapa de secagem para a pós-colheita, este trabalho teve como objetivo avaliar a cinética de secagem de sementes de girassol, em estufa com circulação de ar convectivo e forçado, para diferentes temperaturas, descrever matematicamente e determinar os efeitos da secagem na contração volumétrica das sementes. O delineamento experimental utilizado foi inteiramente casualizado, fatorial (4x3), sendo quatro temperaturas do ar de secagem (45, 55, 65 e 75 °C) e três repetições. A secagem foi realizada até o teor de água das sementes entrarem em equilíbrio higroscópico. A temperatura e o fluxo do ar foram monitorados com auxílio de um psicrômetro e um anemômetro de fio quente, respectivamente. Verificou-se, nos resultados obtidos, que o tempo de secagem foi significativamente (P<0.05) reduzido com o aumento da temperatura do ar de secagem. O modelo de Wang e Sing foi o que melhor ajustou os dados experimentais de secagem. A difusividade efetiva das sementes de girassol variaram de 2.83 a 2.93x10-6 m2 s-1, enquanto que o calor isostérico de sorção foi de 3,725.176 a 3,773.082 kJ kg-1. A redução do teor de água influenciou na contração volumétrica das sementes de girassol, com ênfase para as temperaturas acima de 55 °C. O modelo de Correa et al. foi o que melhor ajustou os dados experimentais de contração volumétrica das sementes de girassol.

PALAVRAS-CHAVE: otimização, pós-colheita, secador.

1 INTRODUCTION

The sunflower (Helianthus annuus L.) stands as the fifth in the world oilseed seed production and fourth in oil production in the world (PESAGRO, 2014). Sunflower oil is one of the fastest meet the standard of quality required by European biodiesel market, also having commercial value greatly increased due to the presence of special compounds that characterize it as a functional food.

After harvesting, the seeds are subjected to pre-processing steps to guarantee quality in subsequent manufacturing processes of the seeds. Drying is an important step in a program of production of sunflower seeds. With the reduction of the water content of the seeds you can store them for a longer time, increasing the marketing and product quality.

However, the drying needs great care due to the transformations, deterioration and losses in the process, with simultaneous heat and mass transfer (CORADI et al., 2014a). To the accomplishment of a proper drying prior knowledge of the material and drying conditions which provide, for example, the temperature of the drying air and seed mass, relative humidity and air flow in the dryer is needed. Carelessness in the drying process can damage cell structures of seeds and denature proteins and cause cracking and change in coloring, reducing the physical and physiological quality (ALMEIDA et al, 2009; CORADI et al., 2014a).

However, in the processing systems of sunflower seeds of the importance of the drying process has been largely ignored. The method employed is more natural, outdoor performed in which the time required for drying is usually long and not always the resulting product is of good quality. Thus, natural drying is giving way to artificial drying techniques, in order to better the quality of the stored product (SILVA, 2008). In Brazil the artificial drying of sunflower seeds, there is little information, particularly the studies on this subject show a certain lack of information, such as drying kinetics, physical characterization and isotherm equilibrium moisture content, so that the optimal drying conditions for domestic cultivars are not well established (SILVA, 2008; CORADI et al., 2014a).

The physical properties of agricultural products have their unrestricted use, being used in the optimization of industrial, design and sizing of equipment used in harvesting operations and post-harvest processes (RESENDE et al., 2008). The knowledge of the physical and mechanical properties of agricultural products is of fundamental importance for conservation

of grain, construction and operation of various equipment used in the main operations of post-harvest products (MIR et al., 2013).

One of the major changes in the physical properties that occur in agricultural products during the drying process is to reduce its external volume, ie shrinkage. The loss of water causes damage to the cell structure of the product leading to a change in shape and decrease

in size of the tissue (MAYOR et al, 2004; GONELI et al., 2011.).

For the development and improvement of equipment used for drying seeds is crucial to the simulation and obtain theoretical information about the behavior of each product during the removal of water. For the simulation, the principle of which is based on the successive thin layers drying the product is used mathematical models that satisfactorily represents the loss of water during drying. The objective of this work was to study the drying kinetics of sunflower seeds in an oven with forced air circulation, with different temperatures (45, 55, 65 and 75 °C), fit the experimental data to non-linear mathematical models and evaluate effects of drying on shrinkage of seeds.

2 MATERIAL AND METHODS

The experiment was conducted at the Federal University of Mato Grosso do Sul (UFMS), Campus of Chapadão do Sul (CPCS) in the year at 2013. The sunflower seeds were harvested at random, and possession of specimens manual separation of impurities was taken damaged seeds. Then, the seeds were dried in a convection oven with forced air ventilation at temperatures of 45, 55, 65 and 75 °C. Drying was carried out until the seeds reach the hygroscopic moisture balance. For each temperature of the drying air drying three tests were performed and for each test, 5 kg of sunflower seeds were used. The temperature and relative humidity were studio monitors, throughout drying with the aid of a psychrometer. The water content of seeds (% w.b.) was determined by weighing 15 g of sample. Then, the samples were placed in an oven with air heating and ventilation regulated at 103 °C ± 1 °C for 24 h, according to the recommendations of (BRASIL, 2009). After the samples were removed and placed in desiccators for cooling. The water content (% w.b.) was determined by mass difference between the initial and the final sample. Tests were performed in three replicates.

The drying curves were fitted to the experimental data using thirteen different semi-empirical and empirical equations discriminated below:

| Equation | Model |
| --- | --- |
|  | Newton | (1) |
|  | Page | (2) |
|  | Page Modified | (3) |
| RU = exp (- a- (a2 + 4 . b . t)1/2) / 2 . b | Thompson | (4) |
|  | Henderson and Pabis | (5) |
|  | Logarithmic | (6) |
|  | Two Terms | (7) |
|  | Two Exponential Terms | (8) |
|  | Wang and Singh | (9) |
|  | Henderson and Pabis Modified | (10) |
|  | Midilli | (11) |
|  | Diffusion approximation | (12) |

wherein RU = moisture ratio (dimensionless) t = drying time (h), k, ko, k1 = drying constant (h-1), a, b, c = model coefficients, n = number of terms of the equation, D = diffusion coefficient (m2 s-1), L = product thickness (m).

For determining the ratios of moisture during drying air under different conditions we used the following expression:

|  | (13) |
| --- | --- |

wherein U* = water content of product (d.b.), Ui* = initial water content of the product (d.b.), Ue* = equilibrium water content of the product (d.b.).

It is usual to consider the value of the diffusion coefficient constant or linearly dependent on the temperature of the air drying. This relationship has been expressed by the Arrhenius model (MOHAPATRA et al., 2005).

(14)

wherein A = constant (m2 s-1), E = activation energy (kJ kmol-1), R = universal gas constant (8,314 kJ kmol-1 K-1), Tabs = absolute temperature (K).

The coefficients of the Arrhenius expression were linearized by applying the logarithm of the form:

(15)

The values of water activity, temperature, and water content equilibrium was obtained from the coffee fruits desorption isotherms, using the model that best fit the experimental data. For the calculation of the integral isosteric heat of desorption we used the following equation:

|  | (16) |
| --- | --- |

wherein Qst = integral isosteric heat of sorption (kJ kg-1), L = latent heat of vaporization of free water (kJ kg-1), Ue* = equilibrium water content (d.b.), a, b = coefficient model.

The free water latent heat of vaporization was obtained using the average temperature by the following equation:

|  | (17) |
| --- | --- |

wherein L = latent heat of vaporization of free water (kJ kg-1), T m = average temperature (°C).

The unitary volumetric shrinkage (Ψg) during the drying of the product was determined by the ratio between the final volume for each water content and the initial volume of the seed. The volume (Vg) of each seed was obtained during the drying process with the aid of a caliper according to the expression proposed by Mohsenin (1986):

Vg = π.a.b.c                                 (18)

6

Wherein a = major axis of the grain (mm), b = mean axis of the seed (mm); c = minor axis of the seed (mm).

| Referência do modelo | Modelo |
| --- | --- |
| Bala and Woods | Ψg = a.{1-exp[b.(U-U0)]} (19) |
| Lang and Sokhansanj | Ψg = a+ß1.(U-U0) (20) |
| Rahman | Ψg = a+ß2.(U-U0) (21) |
| Corrêa et al. | Ψg = 1/[a+b.exp(U)] (22) |
| Line | Ψg = a+b.U (23) |
| Exponential | Ψg = a.exp(b.U) (24) |

wherein Ψg = unit volume shrinkage (decimal), U = water content of the product, the decimal (d.b.), Uo = initial water content of the product, the decimal (d.b.), ß1 = a+b.(UR)+c.(T), a, b, c = parameters that depend on the product, UR = relative humidity (decimal), T = air temperature (ºC), ß2 = volumetric coefficient, dimensionless contraction.

The experimental design was a completely randomized design (CRD) with three tests for each relative humidities and drying temperatures. Nonlinear regressions were performed to adjust the mathematical models analysis based on Quasi-Newton method, using the computer program Statistica 7.0®. To check the fit degree of each model, the significance of the regression coefficient was determined by t-test, adopting the 5% level of probability, the magnitude of the coefficient of determination (R2), the mean relative error values (P), the average estimated error (SE) and the behavior of distribution of residuals was verified. The relative average error and the average error estimated for each model were calculated according to the following expressions, respectively:

|  | (25) |
| --- | --- |
|  | (26) |

Wherein Y = experimentally observed value, = value calculated by the model, n = number of experimental observations, GLR = degrees of freedom of the model (the number of observations minus the number of model parameters).

3 RESULTS AND DISCUSSION

It has been observed, in Figure 1, the influence of air temperature on the kinetics of drying of sunflower seeds. The initial water content of sunflowers seeds was about 46.64 ± 1% (w.b.), and the final water content was 7.62, 7.76, 6.7 and 7.03% (w.b.) at 45, 55, 65 and 75 °C, respectively. The drying times to reach the equilibrium water content for the sunflowers seeds sample were 7.5, 6.5, 5.5 and 4.0 hours at 45, 55 and 75 °C, respectively.

As expected, the dry time decreases with increasing air temperature, so that there is a greater rate of water removal from the seed due to increased moisture gradient between the seed and the air, decreasing the time required to reduce water content to the desired value for storage, a factor noted by several researchers in other agricultural products: grapes (AZZOUZ et al., 2002); red pepper (AKPINAR et al., 2003); prickly pear (LAHSASNI et al., 2004); eggplant (ERTEKIN et al., 2004); parboiled wheat (MOHAPATRA et al., 2005); adzuki beans (ALMEIDA et al., 2009) and jatropha (ULLMANN et al., 2010). In each equal increased temperature interval of 10 °C, the drying time decreased by 13.33% (45 to 55 °C), 15.38% (55 to 65 °C), and 27.27% (65 to 75 °C) correspondingly. The increased temperature interval of 10 °C from 65 to 75 °C has greater effect on the decreasing drying time.

Moreover, the use of higher temperatures allow quicker drying, resulting in a very high humidity difference between the periphery and the center of the seed, generating super drying and problems such as deterioration in the acceleration process. The moisture ratio decreases continuously to the drying progress (Figure 1). It took 4.5, 2.7, 2.3 and 1.7 hours to remove the moisture first half at 45, 55, 65 and 75 °C, respectively, which is about half time of the total drying team. Therefore, half of the total drying team was required to remove the residual moisture due to slower diffusion. These observations are in agreement with previous results on drying of biological products (RESENDE et al., 2008, ULLMANN et al., 2010; CORADI et al., 2014a, CORADI et al., 2014b). It can be observed from Figure 1, that constant rate period was not present during drying of sunflower seeds.

Drying process took place in a falling rate period except a very short accelerating period at the beginning. It can be seen that at higher water content, the increase in temperature has more considerable effect on the drying rates than at lower water content, which was almost negligible at the end. It was further observed that moisture loss was faster at the start of drying than at the end. The reduction in the drying is mainly due to reduction in water content as drying advances. The rate of migration of moisture from inner surface to outer surface decreases at the final stage of drying and hence lower drying rates (RAJKUMAR et al., 2007). In practice, when the heating temperature is higher, then the loss of quality will occur in the sunflower seeds (ALMEIDA et al., 2009). Therefore, with a view of optimization of energy efficiency and the product quality, the heating temperature zone between 65 and 75 °C is a better option for drying sunflower seeds.

Figure 1: Drying curves of sunflower seeds.

The values of the model coefficients are reported in Table 1. The regression analysis was used to set up the relations between these parameters and the temperatures. Thus, the regression equations of these parameters against drying temperature, T (°C) for accepted model. All the coefficients were dependent on drying air temperature. The coefficient ‘a’, ‘c’ varied in nearly sinusoidal shape with temperature, whereas ‘k’, ‘n’ and ‘b’ varied in nearly liner shape. Among the evaluated mathematical models, it was found that the adjusted coefficients of determination, mean relative errors and average estimated errors (Table 3), determined that the Wang and Singh model showed better fit the experimental data to describe the drying process of sunflower seeds, in the temperature range studied (45 to 75 °C).

Table 1: Parameters obtained from models fitted to the data for drying of sunflowers seeds*

| Mathematical models |  |
| --- | --- |
|  | T (0C) | k |  |  |  |  |  |
| Exponen tial | 45 | 0.289430 |  |  |  |  |  |
|  | 55 | 0.464078 |  |  |  |  |  |
|  | 65 | 0.550907 |  |  |  |  |  |
|  | 75 | 0.759458 |  |  |  |  |  |
|  | T (0C) | k | n |  |  |  |  |
| Page | 45 | 0.320876 | 0.921232 |  |  |  |  |
|  | 55 | 0.483817 | 0.953479 |  |  |  |  |
|  | 65 | 0.524997 | 1.064947 |  |  |  |  |
|  | 75 | 0.729502 | 1.092830 |  |  |  |  |
|  | T (0C) | k | n |  |  |  |  |
| Page Modified | 45 | 0.291157 | 0.921232 |  |  |  |  |
|  | 55 | 0.466978 | 0.953479 |  |  |  |  |
|  | 65 | 0.546038 | 1.064947 |  |  |  |  |
|  | 75 | 0.749310 | 1.092830 |  |  |  |  |
|  | T (0C) | a | k |  |  |  |  |
| Henderson and Pabis | 45 | 0.908492 | 0.259222 |  |  |  |  |
|  | 55 | 0.918698 | 0.424069 |  |  |  |  |
|  | 65 | 0.928217 | 0.511096 |  |  |  |  |
|  | 75 | 0.918991 | 0.700129 |  |  |  |  |
|  | T (0C) | a | k | c |  |  |  |
| Logarith mic | 45 | 1.037938 | 0.189904 | -0.15334 |  |  |  |
|  | 55 | 0.903337 | 0.450262 | 0.021476 |  |  |  |
|  | 65 | 0.978978 | 0.437512 | -0.063986 |  |  |  |
|  | 75 | 0.947295 | 0.638264 | -0.035473 |  |  |  |
|  | T (0C) | a | K0 | b | k1 |  |  |
| Two terms | 45 | 0.45446 | 0.259220 | 0.454246 | 0.259220 |  |  |
|  | 55 | 0.459349 | 0.424060 | 0.459349 | 0.424069 |  |  |
|  | 65 | 0.464108 | 0.511096 | 0.464108 | 0.511096 |  |  |
|  | 75 | 0.459495 | 0.700129 | 0.459495 | 0.700129 |  |  |
|  | T (0C) | a | k |  |  |  |  |
| Two exponent tial terms | 45 | 0.520959 | 0.400013 |  |  |  |  |
|  | 55 | 0.498911 | 0.670505 |  |  |  |  |
|  | 65 | 1.512833 | 0.659597 |  |  |  |  |
|  | 75 | 1.586729 | 0.946706 |  |  |  |  |
|  | T (0C) | a | b |  |  |  |  |
| Wang and Sing | 45 | -0.238528 | 0.016447 |  |  |  |  |
|  | 55 | -0.374451 | 0.038879 |  |  |  |  |
|  | 65 | -0.432253 | 0.050702 |  |  |  |  |
|  | 75 | -0.581200 | 0.089508 |  |  |  |  |
|  | T (0C) | a | k | b | k0 | c | k1 |
| Henderson and Modified Pabis | 45 | 0.302837 | 0.259220 | 0.302837 | 0.259220 | 0.302837 | 0.259220 |
|  | 55 | 0.306233 | 0.424060 | 0.306233 | 0.424060 | 0.306233 | 0.424060 |
|  | 65 | 0.309406 | 0.511096 | 0.309406 | 0.511096 | 0.309406 | 0.511096 |
|  | 75 | 0.306330 | 0.700129 | 0.306330 | 0.700129 | 0.306330 | 0.700129 |
|  | T (0C) | a | k | n | b |  |  |
| Midilli | 45 | 0.884174 | 0.211266 | 1.013423 | -0.01038 |  |  |
|  | 55 | 0.882623 | 0.354036 | 1.385108 | 0.017457 |  |  |
|  | 65 | 0.868485 | 0.374479 | 1.491149 | 0.013655 |  |  |
|  | 75 | 0.867934 | 0.592848 | 1.572112 | 0.019016 |  |  |
|  | T (0C) | a | k | b |  |  |  |
| Diffusion approximation | 45 | 0.064322 | 11.54381 | 0.023224 |  |  |  |
|  | 55 | 0.998079 | 0.488154 | -1.129390 |  |  |  |
|  | 65 | -2.421390 | 0.817318 | 0.883372 |  |  |  |
|  | 75 | 9.352686 | 1.084651 | 1.049122 |  |  |  |

*All estimated coefficients were significant at 5% probability by t test.

Table 2: Coefficient of determination (R2), mean relative error (P), estimated values ​​of average error (SE) drying of sunflower seeds due to different temperatures

|  | 45 0C | 55 0C | 65 0C | 75 0C |
| --- | --- | --- | --- | --- |
| R2 (%) |  |
| Exponential | 98.66 | 98.73 | 98.66 | 98.37 |
| Page | 98.80 | 98.77 | 98.73 | 98.47 |
| Page Modified | 98.80 | 98.77 | 98.73 | 98.47 |
| Henderson and Pabis | 99.67 | 99.36 | 99.15 | 98.98 |
| Logarithmic | 99.91 | 99.38 | 99.28 | 99.04 |
| Two Terms | 99.67 | 99.36 | 99.15 | 98.98 |
| Two exponential terms | 98.70 | 98.83 | 98.73 | 98.48 |
| Wang and Singh | 97.80 | 98.51 | 98.75 | 98.55 |
| Henderson and Pabis Modified | 99.67 | 99.36 | 99.15 | 98.98 |
| Midilli | 99.61 | 99.94 | 99.88 | 99.90 |
| Diffusion approximation | 98.93 | 98.98 | 98.73 | 98.46 |
|  |  | SE (decimal) |  |  |
| Exponential | 0.0491 | 0.0704 | 0.0764 | 0.0786 |
| Page | 0.0629 | 0.0804 | 0.0706 | 0.0702 |
| Page Modified | 0.0629 | 0.0804 | 0.0706 | 0.0702 |
| Henderson and Pabis | 0.0761 | 0.0936 | 0.0978 | 0.1029 |
| Logarithmic | 0.0691 | 0.0955 | 0.0912 | 0.0985 |
| Two Terms | 0.0822 | 0.1035 | 0.1109 | 0.1218 |
| Two exponential terms | 0.0586 | 0.0822 | 0.0696 | 0.0685 |
| Wang and Singh | 0.0487 | 0.0745 | 0.0634 | 0.0661 |
| Henderson and Pabis Modified | 0.0900 | 0.1174 | 0.1312 | 0.1573 |
| Midilli | 0.0745 | 0.0969 | 0.0925 | 0.0991 |
| Diffusion approximation | 0.0676 | 0.0871 | 0.0740 | 0.0747 |
|  |  | P (%) |  |  |
| Exponential | 14.24 | 7.67 | 5.84 | 8.51 |
| Page | 12.27 | 8.20 | 5.23 | 7.55 |
| Page Modified | 12.27 | 8.20 | 5.23 | 7.55 |
| Henderson and Pabis | 0.62 | 6.14 | 3.25 | 5.08 |
| Logarithmic | 4.15 | 6.33 | 2.69 | 4.75 |
| Two Terms | 0.62 | 6.14 | 3.25 | 5.08 |
| Two exponential terms | 13.72 | 8.40 | 5.20 | 7.74 |
| Wang and Singh | 23.56 | 10.15 | 8.76 | 10.94 |
| Henderson and Pabis Modified | 7.74 | 6.14 | 8.25 | 5.08 |
| Midilli | 4.18 | 6.95 | 8.79 | 4.70 |
| Diffusion approximation | 10.45 | 8.11 | 5.88 | 7.10 |
| Distribution of residue |  |
| Exponential | A | A | A | A |
| Page | A | A | A | A |
| Page Modified | A | A | A | A |
| Henderson and Pabis | A | A | A | A |
| Logarithmic | A | A | A | A |
| Two Terms | A | A | A | A |
| Two exponential terms | A | A | A | A |
| Wang and Singh | A | A | A | A |
| Henderson and Pabis Modified | A | A | A | A |
| Midilli | A | A | A | A |
| Diffusion approximation | A | A | A | A |

Figure 2 shows the experimental data of water content versus drying time for each drying air temperature adjusted to Wang and Singh model. In Figure 3, the correspondence between the experimental and estimated values ​​and the satisfactory adjustment of the Wang and Singh model to describe the drying of sunflower seeds can be observed. The responses plotted in Figure 5 demonstrates that the data points follows a straight line at 45° angle signifying the suitability of the model in describing the thin layer drying of the sunflower seeds. Similar approach for selecting the model for drying of biological products was reported by RESENDE et al. (2008), GONELI et al. (2011) and CORADI et al. (2014a).

Figure 2: Moisture ratio of sunflower seeds adjusted to the Wang and Singh model.

Figure 3: Experimental data and estimated the moisture ratio, calculated by the model of Wang and Singh.

The results indicated that internal mass transfer resistance controlled the drying time due to which falling rate drying period dominated the drying process. The average values of effective diffusivities of sunflower seeds in the drying process at 45-75 °C varied in the range of 2.83-2.93x10-6 m2 s-1 (Figure 4). It may also be observed from Figure 4 that effective diffusivity increased with the increase in temperature. The results are in agreement with the findings of WANG et al. (2007); RESENDE et al. (2008); GONELI et al. (2011); CORADI et al. (2014b). The evaluated effective diffusivities were within the range of published values ranging from 10-11 to 10-6 for food materials (WANG et al., 2006; RESENDE et al., 2008, CORADI et al., 2014a). Figure 5 shows the values ​​of D presented as "ln D" described as a function of the reciprocal absolute temperature (1/T). The straight line obtained indicates the uniformity of variation of diffusivity with temperature.

Figure 4: Mean values ​​for the effective diffusion coefficient (m2 s-1), due to different air temperatures in the drying of sunflower seeds.

Figure 5: Representation of the Arrhenius relationship for the effective diffusivity

and air temperature drying of sunflower seeds.

In Figure 6 are shown the curves of latent heat of vaporization of water from sunflower seeds at temperatures of 45, 55, 65 and 75 °C. The latent heat of vaporization ranged from 3,725.176 to 3,773.082 kJ kg-1, whereas with the decrease in the equilibrium water content, there was an increase in energy needed for the

evaporation of water from the corn kernels. According to BROOKER et al. (1992), the water content and temperature are the main factors that influence the value of the latent heat of vaporization of water from the product. It is found that with increasing temperature for the same water content, there is a reduction of the latent heat of vaporization. ALMEIDA et al. (2000) studied the latent heat of vaporization of seed cotton and lint without also observed this same behavior. The same results was observed CORADI et al. (2014a) and CORADI et al. (2014b) when studied the latent heat of vaporization in coffee grains and lemon grass plant.

Figure 6: Experimental values ​​and estimated integral isosteric heat of sorption as a function of moisture content equilibrium.

The analysis of the data (Table 3) indicated that the model Correa et al. was the most suitable for mathematical description of the phenomenon of shrinkage of sunflower seeds (Figure 7), showing a high determination coefficient and low values ​​of the mean relative errors and estimated, and yet, all the models showed a random distribution and approximately regular residues (Tables 3 and 4). It has been observed, in Figure 7, in reducing the water content of 0.86 to 0.09 (kg kg-1 dry matter) marked reduction in seed volume, relative to the initial volume occurred at temperatures of 75, 65, 55 and 45 °C.

Table 3: Parameters estimated, coefficient of determination (R²) and distribution of residues of the mathematical models used to describe the shrinkage of sunflower seeds for different temperatures of the drying air

| Mathematical models | Estimation of parameters | R² | Distribution of residuals |
| --- | --- | --- | --- |
| Temperature 45 ºC |
| Bala and Woods | a= 0.92912 b= -18.0258 | 68.23 | T |
| Rahman | a=0.75374 | 98.35 | A |
|  | b= 0.52211 |  |  |
| Correa et al. | a= 1.77125 b= -0.4918 | 98.86 | A |
| Exponencial | a= 0.79186 b= 0.58681 | 98.77 | A |
| Temperature 55 ºC |
| Bala and Woods | a= 0.90889 b= -25.7737 | 28.94 | T |
| Rahman | a=0.78178 | 87.10 | A |
|  | b= 0.419414 |  |  |
| Correa et al. | a= 1.6682 b= -0.41392 | 90.75 | A |
| Exponencial | a= 0.78537 b= 0.478184 | 88.09 | A |
| Temperature 65 ºC |
| Bala e Woods | a= 0.91238 b= -18.7278 | 62.48 | T |
| Rahman | a=0.74456 | 96.00 | A |
|  | b= 0.506803 |  |  |
| Correa et al. | a= 1.79890 b=-0.4999 | 98.03 | A |
| Exponencial | a= 0.75167 b= 0.581219 | 96.65 | A |
| Temperature 75 ºC |
| Bala and Woods | a= 0.90963 b=-17.8313 | 66.13 | T |
| Rahman | a=0.73223 | 96.29 | A |
|  | b= 0.528912 |  |  |
| Correa et al. | a= 1.84398 b= -0.52740 | 98.13 | A |
| Exponencial | a= 0.74023 b= 0.610357 | 96.90 | A |

Table 4: Values ​​of mean relative error (P), estimated values ​​of average error (SE) of drying of sunflowers seeds due to different temperatures

|  | 45 0C | 55 0C | 65 0C | 75 0C |
| --- | --- | --- | --- | --- |
|  |  | SE (decimal) |  |  |
| Bala and Woods | 0.051336 | 0.060971 | 0.0545230 | 0.054501 |
| Rahman | 0.012667 | 0.031287 | 0.0195408 | 0.019595 |
| Correa et al. | 0.007480 | 0.026750 | 0.0137760 | 0.013976 |
| Exponencial | 0.010959 | 0.030143 | 0.0179071 | 0.017941 |
|  |  | P(%) |  |  |
| Bala and Woods | 5.84627 | 1.926450 | 5.1696970 | 5.595600 |
| Rahman | 0.75000 | 0.130000 | 0.1010000 | 0.760000 |
| Correa et al. | 0.32463 | 0.653270 | 0.4535350 | 0.414200 |
| Exponencial | 2.20796 | 4.005950 | 3.3492420 | 3.357070 |

Figure 7: Volumetric shrinkage of sunflower seeds adjusted to the Corrêa et al. model along of the drying with different air temperatures.

The drying temperature of 45 °C was reduced to less than the volume of the seed, possibly by the low rate of water removal, causing stiffening of the integument, which hindered the contraction of the seeds and, accordingly, reduced to a lesser extent their volume. Whereas, temperatures of 65 to 75 °C to greatest influence on volume, once the water is removed quickly and seeds contracted orthogonal axes in accordance with the reduction of water content. Corroborating SIQUEIRA et al. (2011) who found that the decrease in the geometric mean diameter of the seeds is proportional to the reduction of the water content and also depending on the drying condition, that is, the drying air temperature.

4 CONCLUSION

The drying time was significantly reduced with increasing temperature of the drying air. The model of Wang and Sing was that better adjusted to experimental drying data. Effective diffusivity of sunflower seed ranged from 2.83 to 2.93x10-6 m2 s-1, while the isosteric heat of adsorption was 3,725.176 to 3,773.082 kJ kg-1. Reducing the water content influenced the shrinkage of sunflower seeds, with emphasis on temperatures above 55 °C. The model Correa et al. was that better adjusted to experimental data of volumetric shrinkage of sunflower seeds.

5 REFERENCES

AKGUN, N. A.; DOYMAZ, I. Modeling of olive cake thin-layer drying process. J. Food Eng. v. 68, n. 4, p. 455-461, 2005.

ALMEIDA, F. de A. C.; MATA, M. E. R. M. C.; CORRÊA, P. C. Isotermas de Adsorção e calor latente de vaporização de sementes de algodão, com e sem línter. Revista Oleaginosas e Fibrosas, Campina Grande, v. 4, n. 3, p. 225-234, 2000.

ALMEIDA, D. P. et al. Cinética de secagem do feijão adzuki (Vigna angularis). Global Science and Technology. v. 2, n. 1, p. 72-83, 2009.

BRASIL. Ministério da Agricultura e Reforma Agrária. Regras para análise de sementes. Brasília: SNDA/DNDV/CLAV, 2009.

BROOKER, D. B.; BAKKER-ARKEMA, F. W.; HALL, C. W. Drying and storage of grains and oilseeds. Westport: The AVI Publishing Company, 1992, 450p.

CORADI, P. C.; MELO, E. C.; ROCHA, R. P. Evaluation of electrical conductivity as a quality parameter of lemongrass leaves (Cymbopogon Citratus Stapf) submitted to drying process. Drying Technology (Online), v. 32, n. 8, p. 969-980, 2014a.

CORADI, P. C.; BORÉM, F. M.; REINATO, C. H. Coffee cherries drying process and the influence of environment relative humidity in the mathematical modeling, moisture content, and enthalpy of vaporization. Energia na Agricultura (UNESP. Botucatú. CD-Rom), v. 29, n. 2, p. 148-157, 2014b.

GONELI, A. L. D. et al. Contração volumétrica e forma dos frutos de mamona durante a secagem. Acta Scientiarum. Agronomy, v. 33, n.1, p. 1-8, 2011.

ERTEKIN C, YALDIZ, O. Drying of eggplant and selection of a suitable thin layer drying model. J. Food Eng. v. 63, n. 3, p. 349-359, 2004.

LAHSASNI, S. et al. Drying kinetics of prickly pear fruit (Opuntia ficus indica). Journal of Food Engineering. v. 2, n. 2, p. 73-179, 2004.

MAYOR, L.; SERENO, A. M. Modeling shrinkage during convective drying of food materials: a review. Journal of Food Engineering, v. 61, n. 3, p. 373-386, 2004.

MIR, S. A.; BOSCO, S. J. D.; SUNOOJ, K. V. Evaluation of physical properties of rice cultivars grown in the temperate region of India. International Food Research Journal, v. 20, n. 4, p. 1521-1527, 2013.

MOHAPATRA, D.; RAO, P. S. A thin layer drying model of parboiled wheat. Journal of Food Engineering. v. 34, n. 4, p. 513-518, 2005.

MOSHENIN, N. N. Physical properties of plant and animal materials. New York, USA. 1986, 841p.

PESAGRO. Empresa de Pesquisa Agropecuária do Rio de Janeiro, disponível em, <http://www.pesagro.rj.gov.br/downloads/maisnoticia_jul07.pdf>. Acesso em 21/04/2014.

RAJKUMAR, P. et al. Drying characteristics of foamed alphonso mango pulp in a continuous type foam mat dryer. J. Food Eng. v. 79, n. 4, p. 1452-1459, 2007.

RESENDE, O. et al. Modelagem matemática do processo de secagem de duas variedades de feijão (Phaseolus vulgaris L.). Revista Brasileira de Produtos Agroindustriais. v. 10, n. 1, p. 17-26, 2008.

SILVA, J. S. Secagem e Armazenagem de Produtos Agrícolas. Viçosa, Aprenda Fácil, 2008.

SIQUEIRA, V. C.; RESENDE, O.; CHAVES, T. H. Contração volumétrica dos frutos de pinhão-manso durante a secagem em diversas temperaturas. Revista Brasileira de Armazenamento, Viçosa, v. 36, n. 2, p. 171-178, 2011.

ULLMANN, R. et al. Qualidade das sementes de pinhão manso submetidas à secagem em diferentes condições de ar. (Quality Jatropha seeds dried in different conditions of air). Revista Ciência Agronômica. v. 41, n. 3, p. 442-447. 2010.

YALÇIN, Ý.; ÖZARSLAN, C.; AKBAÞ, T. Physical properties of pea (Pisum sativum) seed. Journal of Food Engineering, v. 79, n. 2, p. 731-735, 2007.

WANG, Z. et al. Mathematical modeling on hot air drying of thin layer apple pomace. Food Res. Int. v. 40, n. 1, p. 39-46, 2006.

WANG, Z. et al. Mathematical modeling on thin layer microwave drying of apple pomace with and without hot air predrying. J. Food Eng. v. 80, n. 2, p. 536-544, 2007.

# Footnotes

*Engenheiro Agrícola, Professor Adjunto II, Universidade Federal de Mato Grosso do Sul (UFMS), Campus Chapadão do Sul, Mato Grosso do Sul, Brasil, Phone: (0XX67) 3562-6300, paulo.coradi @ufms.br

Estudante de graduação em Agronomia, Bolsistas de Iniciação Científica, Universidade Federal de Mato Grosso do Sul (UFMS), Campus Chapadão do Sul, Mato Grosso do Sul, Brasil.